LECTURE 10:

Syeda Zoha Haider

Outside the chip, there are many concerns, such as, I/O Circuits, Bonding, Packaging, and Board. IC package is an interface between the chip and the external world. The main purposes of the package is to provide physical, electrical, and temperature protection. The package ensures an electrical connection and physical connection from chip to board. It protects the chip from high voltages from the external environment. It physically protects the chip as well as provides it with thermo isolation.

The requirements of a package are electrical, mechanical, thermal, cost, and interface related. It is necessary to have capacitance, resistance, inductance and impedance tuning. It is also essential to have a large number of I/O pins and to have Die/Bond protection. During packaging, heat removal is also taken into consideration while ensuring that the cost is as minimum as possible.

There are 4 different types of Packages: Dual Inline Package (DIP), Quad Flat Package (QFP), Pin Grid Array (PGA), and Ball Grid Array (BGA). DIP was the simplest package that was used in the earlier years. The problem with that was it didn’t have enough I/Os/ So, QFP was developed. This package had more connections as compared to DFP, and soldering and making connections was very easy with it. However, the number of I/Os were still unsatisfactory, so PGA was made, and then BGA.

There are two main approaches to making IC to Package connection: Wire Bonding and Flip Chip.
In Wire Bonding, the die is placed on a solder that it can be held on to. The die is soldered with a piece of metal, usually gold, and is tied to the pin. Thin gold wire is used to make these connections. It has long, high RLC wires. Its cheap. In Flip Chip, the chip is placed on solder bumps. The array of paads are on the package itself. It looks like a BGA. This lets us connect the bonds anywhere. We can have high-fanout signals placed near wherever they are needed chip, and provide power and ground wherever it is required. It reduces long routes. The chip is just placed on the substrate and then it is heated, and all the connections are made. We can have many more pins. It is, however, very expensive. While designing a wire bond package, it is necessary to ensure that there are no crossing of bond wires, maximum length of wires, maximum angle of wires, and maximum spacing. It is required to make a physical connection to the bonding wire. So, for wire bond packaging we use landing pads. Whereas, for flip chip packaging, solder bumps are used. Bonding pads are then connected to I/O circuits.

I/O Circuits should be able to drive big loads, have consistent voltage, low switching noise, and ESD protection. Goals of I/O Design is to reduce delay to and from outside world , have high drive current capability, match impedance to load, Level shifting of voltages (i.e.1.2V inside/3.3V outside) , meet specifications of Interfaces, reduce power and provide high voltage tolerance. There are different types of I/O Cells: Standard and Special. Standard can be further split down into digital, analog, and power. Special I/O Cells can be split into SSTL, HSTL, LVDS, etc.

The guidelines during I/O design are to put as many mutual capacitance as possible between IC supply voltages, put as many supply voltage pins as possible, put supply and ground supply voltages as close to each other as possible, provide separate supply voltages for the core and I/Os, reduce inductances as much as possible by using as short transmission lines as possible, reduce signal rate as much as possible. However be careful as the reduction of signal rate leads to signal weakening, and experiments show that those noises can have definite affect on the given I/O cells. Pad Configurations can be In-line, Staggered, Circuit Under Pad (CUP), Flip Chip with RDL.

LECTURE 11:

The basic way to run STA is to check Max-delay (setup) checks are run on worst-case (slow) conditions and Min-delay (hold) checks are run on best-case (fast) conditions. However, it doesn’t take into account variation that can occur across the chip, for example, due to a temperature variance. There are different types of On Chip Variations: Spatial Variation, during setup, and during hold. Spatial variation happens because chips are big and delay elements can be far from each other. Process/Voltage/Temperature (PVT) variation can affect different parts of the timing path in opposite directions. We don’t assume the worst possible case because during setup, the launch (data) path is extra slow The capture (clock) path is super fast. During hold, the launch (data) path is super fast. The capture (clock) path is extra slow.

A common practice in VLSI design implementation is to be over pessimistic. If you are optimistic, your chip may not work. If you over-design, your yield will go up. However, over pessimism causes problems, such as, time-to-market increases, performance is hindered, less efficient in all parameters: size, power, performance

OCV is too pessimistic. To limit the pessimism of OCV, Clock Re-convergence Pessimism Removal is applied. This basically removes the derating from the clock path shared by both the launch and capture paths. CPPR helped, but the derates are still bad. All paths don’t have the same derate. But statistical behavior is hard to compute. Worst-case conditions are dependent on the distance between gates on the path, and depth (number of stages) of the path. This is the principle behind Advanced On-Chip Variation. Parametric on-chip variation (POCV) AOCV is still too pessimistic Variation is statistical and is different for each gate. In POCV, distribution for each gate is given in the library. Path-based Analysis (PBA) also helps with pessimism removal. Due to long run times, STA is usually run with Graph-based Analysis (GBA). GBA chooses the worst case propagation from all inputs through a gate. PBA chooses the propagation of the specific path. This results in a 10X longer run time but highly reduced pessimism.

 Another big issue in modern VLSI design is aging. Device characteristics change over time. In order to deal with aging effects, operate with low VDD, model aging as an additional timing margin, use aged library models for signoff timing and add aging sensors and adjust frequency/voltage for compensation.

Chip Finishing for Signoff includes insertion of fillers and DeCaps, application of Design for Manufacturing (DFM) and Design for Yield (DFY) rules, Antenna checking, Metal filling and slotting for metal density rules, IR Drop and Electromigration Analysis, Logic Equivalence, Layout (Physical) Verification and adding Sealring.